## Slide 1: GSA Grasshopper Plugin
SSN.E - Parametric Design for Structures
10th February 2021
Kristjan Nielsen
Annotation text
1
Highlight something
Dim
2
Highlight something

## Slide 2: Overview
Workflow and Apps EcoSystem

## Slide 3
Speckle Server
Local computer
Overview Workflow and Eco system of connected applications
Rhino
Grasshopper
GsaAPI
Headless GSA
GSA Grasshopper
GSA
Speckle
Cloud
Total Design Automation
ArupCompute
DesignCheck
AdSec

## Slide 4: Installing Plugin
Using Rhino Package Manager

## Slide 5
Installing GSA-Grasshopper
1
2
3
Rhino6 Command:
TestPackageManager

## Slide 6
Installing GSA-Grasshopper

## Slide 7: Overview
Plugin Sub-Categories

## Slide 8
Node Res.
1D Results
2D Results
Load
GridPlnSrf
Node
Element1D
Element2D
Member1D
Member2D
Member3D
Section
Prop2D
Offset
Spring
Bool6
GSA Model
Open Model
Save Model
GSA Model
Overview Plugin workflow
Model
Properties
Geometry
Loads
Analyse
Results

## Slide 9
Node Res.
1D Results
2D Results
Load
GridPlnSrf
Node
Element1D
Element2D
Member1D
Member2D
Member3D
Section
Prop2D
Offset
Spring
Bool6
GSA Model
Open Model
Save Model
GSA Model
Overview Plugin workflow
Model
Properties
Geometry
Loads
Analyse
Results

## Slide 10: Model

## Slide 11
Model tab

## Slide 12
Open Model & Get Geometry

## Slide 13
GSA Grasshopper Parameters

## Slide 14
GSA Grasshopper Parameters – GSA Reference

## Slide 15: Properties

## Slide 16
Properties tab

## Slide 17
Create Properties Examples [Live Demo]

## Slide 18
Create Profile

## Slide 19
Create Geometric Section

## Slide 20
Create and Edit Bool6 Parameter

## Slide 21
Bool6 and Offset Properties

## Slide 22: Geometry

## Slide 23
Geometry tab

## Slide 24
Rhino/GH Geometry correlation with GSA Geometry
0D
Node
1D
2D
1D
2D
3D
Element1D
Element2D
Member1D
Member2D
Member3D
Point3D
(x, y, z)
Line
(x1, y1, z1, x2, y2, z2)
Mesh
(Verticies, FaceList)
PolyCurve (Arc or Polyline)
(TopologyList)
Planar BRep (Edges, inc.Lines, inc.Pts)
Solid (Closed Mesh) (Verticies, FaceList)
BRep auo-capped if not closed
BRep auto-converted to mesh
BRep auto-converted to planar
Nurbs edges and incl. Crvs auto-converted to Arcs and Lines
Inclusion Pts and Crvs auto-projected onto plane
Nurbs crv auto-converted to Arc or Polyline

## Slide 25
On-the-fly conversions

## Slide 26
On-the-fly conversions with Existing GSA Model

## Slide 27
Create Geometry Examples [Live Demo]

## Slide 28
Create Member2D with inclusion Pt and Crv Example

## Slide 29
Create Member3D Example

## Slide 30
Create and Edit Member1D and Member2D Mesh Size [Live Demo]

## Slide 31
GH-Transform GSA Geometry and Colour Examples [Live Demo]

## Slide 32: Working with IDs

## Slide 33
Working with IDs – No ID set
1
2
3
Section Properties in existing GSA Model. The model contains 4 sections
Create a new Section without setting the ID
Combine Existing GSA Model with new Property in Analysis component. Use Save to save the GSA Model with changes
4
Open the modified GSA Model in GSA. The Section Library now includes the new Section appended to the existing 4

## Slide 34
Working with IDs – SET ID
1
2
3
Section Properties in existing GSA Model
Set ID to a number bigger than 0 (zero) overwrite existing Property
Combine Existing GSA Model with new Property in Analysis component. Use Save to save the GSA Model with changes
4
Open the modified GSA Model in GSA. The old second with ID=2 has been replaced by the new Section

## Slide 35
GridPlnSrf
Node
Element1D
Element2D
Member1D
Member2D
Member3D
Section
Prop2D
Working with IDs – GSA Parameters with IDs
Properties
Geometry
Loads
GSA Grasshopper GridPlaneSurface has ID for both GridPlane and GridSurface, but not for Axis
Also note that Loads does not have ID and will thus always be appended

## Slide 36: Properties and Geometry
Relationship between Section/Prop2D and Elements/Members

## Slide 37
Overview relationship Section/Prop2D with Elements/Members
Properties
Geometry
Section
Element1D
Member1D
Element2D
Member2D
Prop2D
1D
2D

## Slide 38
Workflow Example 1
1
2
Create new Section without ID (ID = 0). Section will be appended to end of existing Section Library
Create new Element1D from Line and input PB to attach this section to the Element1D object. The Element1D object will carry the Section with it around the GH script
3
Assembling the model using Analysis Component can be done without inputting Section in “Prop”

## Slide 39
Workflow Example 2
1
2
Create new Section with unique ID (ID = 42 here). Section will be set (and overwrite existing Section) in Section Library
Create new Element1D from Line and input Integer (42 here) in PB-input to make reference to a Section number in the Section Library. Section may already exist in a GSA model and does not need to be created in Grasshopper
3
Assembling the model using Analysis Component should be done with both Prop and Geo inputs, unless Section already exist in an existing GSA model

## Slide 40
Relationship between Section/Prop2D and Elements/Members
Create components
Edit components
1D
2D

## Slide 41
Applies when opening Existing Model as well
Edit components
GetGeometry
OpenModel
EditMem1D
EditMem2D
EditProp2D
EditSection
SectionProperties

## Slide 42: Loads
Typical referenced by object

## Slide 43
Load tab

## Slide 44
Typical Loads - Gravity
LC default = 1
List of elements default = “All”
Name is optional (default empty)
Gravity vector default = (0, 0, -1)

## Slide 45
Typical Loads – Node Load
Direction input: x, y, z, xx, yy, zz Default = z
List of nodes in model to apply load to
Dropdown UI to change Load Type

## Slide 46
Typical Loads – Beam Load
Dropdown UI to change Load Type
Axis: Global/Local - Default = Global
Direction: x, y, z, xx, yy, zz - Default = z
Projection: True/False - Default = False
Load Value and Position (t) adjusts with selected Load Type

## Slide 47
Typical Loads – Face Load
Dropdown UI to change Load Type
Axis: Global/Local - Default = Local
Direction: x, y, z, xx, yy, zz - Default = z
Projection: True/False - Default = False
Load Value and Position (t) adjusts with selected Load Type

## Slide 48: Grid Loading
Automatically Expanded loads

## Slide 49
GridPlaneSurface Parameter – Grid Plane

## Slide 50
GridPlaneSurface Parameter – Grid Surface

## Slide 51
GridAreaLoad Wind Load Generator Example [Live Demo]

## Slide 52: Analyse

## Slide 53
Analysis tab

## Slide 54
GSA Grasshopper Workflow
Node Res.
1D Results
2D Results
Load
GridPlnSrf
Node
Element1D
Element2D
Member1D
Member2D
Member3D
Section
Prop2D
Offset
Spring
Bool6
GSA Model
Open Model
Save Model
GSA Model
Model
Properties
Geometry
Loads
Analyse
Results
Analysis tasks coming soon

## Slide 55: Results

## Slide 56
Results tab

## Slide 57
Analysis of simple cantilever [Live Demo]

## Slide 58
Analysis of 4 point surface [Live Demo]

## Slide 59: Limitations

## Slide 60
Known bugs and limitations
Current state of the plugin is Alpha – things might break, and things will change. (It is however getting close to a final state with the current components)
Materials cannot be created at all – GSA-Grasshopper material parameter to be developed
Analysis tasks cannot be created – GSA-Grasshopper analysis task parameter to be developed
Spring parameter not working at all (placeholder in plugin for now)
Prop2D thickness cannot be set
Releases cannot be set in neither Element1D or Member1D
CreateProfile Catalogue lookup sometimes fails
OpenModel sometimes returns empty model when re-using the button
Settings for Elements and Members not fully covered
Tolerance cannot be set for Grid Surface
Meshing of 2D Members can become really slow on medium-large models
Using filters on GetGeometry not covering PB-terminology
Results components are WIP, use with care (e.g. proper self-checking of results values)
No results for Load Combinations are available
Units cannot be change (placeholder in plugin for now). Use [kN-m] for now
Titles cannot be set (placeholder in plugin for now)
No graphical visualisation of restraints, releases or cross-section available
Conflict with referenced dll when running analysis and having Karamba3D plugin installed

## Slide 61
Installing GSA-Grasshopper
1
2
3
Rhino Command:
TestPackageManager