## Slide 1: GSA for Grasshopper
Use-cases, namespace overview and component set
Draft 23rd July
Update 28th August
Update 21st September
Kristjan Nielsen
Oasys GSA

## Slide 2
Use cases
Simplified, three main use cases has been defined to try cover all use cases
Create a new model
  Geometry (0D, 1D and 2D – analysis and design layer)
  Meta data (support conditions, end releases, springs, offset; sections and material)
  Analysis (loads, load cases, load combinations, analysis tasks and solvers)
  Save GSA file (and speckle)
Modify an existing model
  Open GSA file (and speckle)
  Geometry (0D, 1D and 2D – analysis and design layer)
  Meta data (support conditions, end releases, springs, offset; sections and material)
  Analysis (loads, load cases, load combinations, analysis tasks and solvers)
View analysis results
  Display and expose result values (node reactions and displacement; beam/shell forces and moments, displacement and stresses; member results)
Overview

## Slide 3
GhSA namespace
Helper classes
GsaImportConvertions
GsaModelConvertions
RhinoConvertions
Grasshopper components layer
Handles input and output, solve instance and custom UI
Grasshopper Persistent Parameters
Turns custom objects into Grasshopper readable & visualisable parameters
Persistent Goo Params
GsaBool6Goo
GsaOffsetGoo
GsaSpringGoo
TBD: load, section, material, etc
Persistent GeometryGoo Params
GsaNodeGoo
GsaElement1dGoo
GsaElement2dGoo
GsaMember1dGoo
GsaMember2dGoo
C# Object Types / Classes
Custom objects holding a combination of information to be passed around
Persistent GeometryGoo Params
GsaNode
GsaElement1d
GsaElement2d
GsaMember1d
GsaMember2d
GsaBool6Goo
GsaOffsetGoo
GsaSpringGoo
To be done:
GsaSection
GsaMaterial
GsaLoad
GsaLoadCase/Combination?
GsaAnalysisType
GsaAPI
Helper classes
Custom UI
Ribbon layout
Graphic buttons
Colours
User

## Slide 4
Grasshopper Parameters
Grasshopper passes around copies
  Point -> move = original + moved
  Changes downstream should not effect original
GSA must provide some new Grasshopper Parameters (”Object Types”?)
  GsaAPI.Model
    GsaAPI.Node
      GsaAPI.Bool6
    GsaAPI.Member
      GsaAPI.Bool6
      GsaAPI.Offset
    GsaAPI.Section
    GsaAPI.Load
Some GSA Object Types can be mapped directly to existin GH Parameter, like Axis -> Plane
GSA Parameter Object Types
Parameter Object Type:
Node
GsaAPI.Node
GsaAPI.Axis
Parameter Object Type:
Bool6
GsaAPI.Bool6
Parameter Object Type:
Model
GsaAPI.Model
What happens if we pass around GsaAPI.Model 15 times in a script?

## Slide 5
Grasshopper Parameters
GsaBool6
Parameter Object Type:
GsaBool6
bool GsaBool6.X
bool GsaBool6.Y
bool GsaBool6.Z
bool GsaBool6.XX
bool GsaBool6.YY
bool GsaBool6.ZZ

## Slide 6
Grasshopper Parameters
GsaSpring
Parameter Object Type:
GsaSpring
double GsaSpring.X
double GsaSpring.Y
double GsaSpring.Z
double GsaSpring.XX
double GsaSpring.YY
double GsaSpring.ZZ

## Slide 7
Grasshopper Parameters
GsaOffset
Parameter Object Type:
GsaOffset
double GsaOffset.X1
double GsaOffset.X2
double GsaOffset.Y
double GsaOffset.Z

## Slide 8
Grasshopper Parameters
GsaNode
Parameter Object Type:
GsaNode
GsaAPI.Node GsaNode.node
Rhino.Point3d GsaNode.Point
int GsaNode.ID
Rhino.Plane GsaNode.localAxis
GsaSpring GsaNode.Spring

## Slide 9
Grasshopper Parameters
GSA Parameter: Gsa Node
Parameter Object Type:
Node
GsaAPI.Node (Point3d)
GsaAPI.Axis (Plane)

## Slide 10
Grasshopper Parameters
GsaElement1d
Parameter Object Type:
GsaElement1d
GsaAPI.Element GsaElement1d.Element
Rhino.LineCurve GsaElement1d.Line
int GsaElement1d.ID
GsaBool6 GsaElement1d.ReleaseStart
GsaBool6 GsaElement1d.ReleaseEnd

## Slide 11
Grasshopper Parameters
GSA Parameter: Gsa Element 1D
Parameter Object Type:
Element1D
GsaAPI.Element (Line)

## Slide 12
Grasshopper Parameters
GsaElement2d
Parameter Object Type:
GsaElement2d
List<GsaAPI.Element> GsaElement2d.Elements
Rhino.Mesh GsaElement2d.Mesh
List<Rhino.Point3d> GsaElement2d.Topology
List<int> GsaElement2d.ID
List<List<int>> GsaElement2d.TopoInt

## Slide 13
Grasshopper Parameters
GSA Parameter: Gsa Element 2D
Parameter Object Type:
Element2D
List<GsaAPI.Element> (Mesh)

## Slide 14
Grasshopper Parameters
GsaMember1d
Parameter Object Type:
GsaMember1d
GsaAPI.Member GsaMember1d.member
Rhino.PolyCurve GsaMember1d.PolyCurve
List<Rhino.Point3d> GsaMember1d.Topology
List<string> GsaMember1d.TopologyType
GsaBool6 GsaMember1d.ReleaseStart
GsaBool6 GsaMember1d.ReleaseEnd
To be added:
var (int / GsaSection) GsaMember1d.Section

## Slide 15
Grasshopper Parameters
GsaMember2d
Parameter Object Type:
GsaMember2d
GsaAPI.Member GsaMember2d.member
Rhino.Brep GsaMember2d.Brep
List<Rhino.Point3d> GsaMember2d.Topology
List<string> GsaMember2d.TopologyType
List<List< Rhino.Point3d >> GsaMember2d.VoidTopology
List<List<string>> GsaMember2d.VoidTopologyType
List<Rhino.PolyCurve> GsaMember2d.InlusionLines
List<List< Rhino.Point3d >> GsaMember2d.IncLinesTopology
List<List<string>> GsaMember2d. IncLinesTopologyType
List<Rhino.Point3d> GsaMember2d.InclusionPoints
To be added:
var (int / GsaSection) GsaMember1d.Section

## Slide 16
Components
Simple example: Bool6 info
Name, Nickname and description
Plugin name and Subcategory
should call Ribbon helper class
Unique GUID
Position on Ribbon dropdown
Output as Goo-type
Output each individual setting

## Slide 17
Components
Custom GUI example: Bool6 create
As simple component
To create custom UI we must override “CreateAttributes”
Call Bool6CompomentUI function with an action/function (“setBool”) that can set this components variables
Set of parameters outside of solve-instance that can be set by UI
We need to add this (de)serialisation section to be able to save the user-input to made with the custom UI interface, otherwise the component will reset to default settings when a saved grasshopper file is reopened

## Slide 18
Components
Custom GUI example: Bool6 create
Use Grasshopper to convert whenever possible; this means fx that a Boolean input can also be 0 or 1, but more expanded for geometry types
As simple component

## Slide 20
Use cases
Geometry:
  Point -> Position
  Plane -> Location axis
MetaData:
  Restraints: bool6
  Spring property (int or spring object?)
  Mass property
  Damper property
  Local element size
  Other: name, colour, connected elements, axis property – necessary?
Support component inputs:
  Point(s)
  Plane(s) – must be passed around as Axis until model assembly?
  Bool6 list to override UI input?
  Spring(s) – must be passed around as SpringProp until model assembly?
Modify Node component:
  Set/Change mass, damper, local element size, name, colour, axis
Create: Nodes
Support
Pt
Pl
Res
Spr
Restraints
x
y
z
xx
yy
zz
Node
Free
Pin
Fix
Parameter Object Type:
Node
GsaAPI.Node
GsaAPI.Axis
Boolean 6
x
y
z
xx
yy
Set all
x
y
z
xx
yy
zz
zz
Bool6
Parameter Object Type:
Bool6
GsaAPI.Bool6

## Slide 21
Use cases
Geometry:
  Line, Arc, Polyline – alternative also Curve with automatic conversion to lines and arcs?
  Topology list to be passed around as Points until model assembly?
MetaData:
  Property (int or property object?)
  MemberType (list input, dropdown UI, ??)
  End releases (2x bool6)
  Offset – own parameter object type
  Orientation (node (int or node object type) and angle(double))
  MeshSize (double)
  Mesh with others (bool)
Create Member1D component inputs:
  Curve
  Property
  MemberType
  Releases
  Offset
Modify Member1D component:
  Set/Change: Inclusion points, Mesh with others, MeshSize, Name, Colour, Orientation
Create: 1D Member
Modify Member 1D
Crv
Prop
Typ
Rel1
Offs
Mem1D
Type | Generic 1D
Releases
x
y
z
xx
yy
zz
S
x
y
z
xx
yy
zz
E
Member 1D
Crv
Prop
Typ
Rel
Offs
Mem1D
Releases
x
y
z
xx
yy
zz
S
x
y
z
xx
yy
zz
E
Analysis
Design
Layer
Member 1D
Crv
Prop
Typ
Rel1
Rel2
Mem1D
Offs
Boolean 6
x
y
z
xx
yy
Bool6
Set all
x
y
z
xx
yy
zz
zz
Offset
X1
X2
Y
Z
Offset
Simple option
Another option
Comined analysis/design option
Rel2
Parameter Object Type:
Member
GsaAPI.Member
List<Node>
Prop
Material
Parameter Object Type:
Offset
GsaAPI.Offset
M1D
Crv
Prop
Mem1D
Generic 1D
Releases
x
y
z
xx
yy
zz
S
x
y
z
xx
yy
zz
E
Type
Modify Member 1D
M1D
Prop
Typ
Rel1
Offs
Rel2
MsO
MSz
OriA
M1D
Prop
Typ
Rel1
Offs
Rel2
MsO
MSz
OriA
OriN
OriN
Simple create
Extended modify

## Slide 22
Use cases
Create: Open model

## Slide 23
Use cases
The components have been developed to sit in six categories, both inheriting the way GSA is structured and supporting the natural workflow of creating an FE model:
Geometry (create/initialise model)
  New model from geometry (elements, members, supports, offsets, releases)
  Open exsting GSA model
Properties: Materials and Sections
Loads
Analysis
Results
Output (save file / open in GSA, export to other program, send to speckle)
Create // Modify // Results

## Slide 24
1 Geometry
Workflow
6 categories
Add
Open
Offset
2 Properties
3 Loads
Gravity
4 Analyse
Analyse
Tasks
Combinations
Profile
Material
Sec 1D
Sec 2D
Support
Node
Beam
Face
5 Results
Beam
Face
6 Output
Save
Speckle

## Slide 25
1 Geometry
Components
1 Geometry: Open component
Add
Open
Offset
Support
”Open” component:
Right click to get options menu
  Select gwb file through windows explorer (handy for new GH users)
  Open and import geometry
  Just open
Settings
  Join meshes (GSA works with single faces, use build-in join routine to combine faces into connected meshes)
  Import from lists – let you use the known text filtering syntax (”PB1 to PB4” etc)
Message displayed at bottom of component with information about the model:
  Empty model // Model not analysed // Model has results
The right-click menu for options

## Slide 26
Components
1 Geometry: Open component

## Slide 27
1 Design
Components
1 Geometry: Open component
Add
Open
Offset
Support
”Open” component:
Importing geometry
  Points not imported by default (slows things down and is generally not that useful)
  1D analysis elements imported as lines
  2D analysis elements imported as mesh and optionally joined
Geometry is sorted according to their properties
  All elements of property X will be in branch (X-1) in grasshopper
GSA 2D Elements (1-based)
GH Data tree output (0-based index)
GSA Section Library (1-based)

## Slide 28
1 Design
Components
1 Geometry: Add component
Add
Open
Offset
Support
”Add” component:
The main design component – users can generate all the required geometry from this single component. Must be able to handle simple tasks, explicit/detailed stuff and write to both analysis and design layer.
Right click to get menu options:
  Design layer (default, simple inputs for curves, breps/surfaces and mesh size)
  Design layer // expert mode (all settings for members become available)
  Analysis layer (three simple inputs for analysis: nodes, lines, meshes)
The two main component flavours
The right-click menu for options

## Slide 29
Components
1 Geometry: Add component / 1D member properties

## Slide 30
Components
1 Geometry: Add component / 2D member meshing

## Slide 31
1 Design
Components
1 Geometry: Add component / Expert mode
Add
Open
Offset
Support
”Add” component:
Creates a new empty GSA model to write to
Members/elements with properties corrosponding to the input branch (similar to the Open component methodology)
Nurbs automatically converted to polygons with a preset convertion method (using Rhino Convert Method)
When topology is created nodes are being checked for duplicates with a set tolerance distance against all existing model nodes
Members/elements/nodes are added to the model
For both Design Layer options, the last step is to create elements from members
Output is a GSA model as it is not possible to create elements/members referring to node coordinates but to topology. A single output model was chosen instead
Curves/Lines
Brep/surfaces
Include points; to include in mesh
Include lines; to include in mesh
Mesh size 1D members
Type 1D members
Analysis type 1D members
Offset
Start Member End Condition
End Member End Condition
Group 1D
Name 1D
Mesh size 2D members
Type 2D members
Analysis type 2D members
Offset
Group 2D
Name 2D
Tolerance
Offset not working atm due to missing API function/bug
Support not working atm due to API bug
Design Layer // Expert mode

## Slide 32
Components
2 Properties: Section1D component
”Section1D” component:
Creates a Section from profile input
Default material (steel)
”Profile” component (to be developed):
Method to look up catalogue sections
Possibility to input drawn closed curve
Custom profile copying the logic of the text input (e.g. Something that automatically writes the text string ”STD I 500 400 20 10”.
Section1D component
2 Properties
Profile
Material
Sec 1D
Sec 2D

## Slide 33
Components
3 Loads: Gravity component
”Gravity” component:
Creates a new GravityLoad
Default to z = -1 factor
Can be altered with the known GSA-like input methods
Gravity load with odd inputs
3 Loads
Gravity
Node
Beam
Face
Gravity load default

## Slide 34
Components
3 Loads: NodeLoad component
”NodeLoad” component:
Creates a new NodeLoad from a nodelist and load value
Default direction z
3 Loads
Gravity
Node
Beam
Face
NodeLoad component

## Slide 35
Components
3 Loads: BeamLoad component
”BeamLoad” component:
Right-click menu to toggle between load types: Point, Uniform, Linear, Patch or Triliniar
Static inputs for load case, element list, axis, direction and projection (with defaults)
Input adapts to the selected load type as known from GSA:
3 Loads
Gravity
Node
Beam
Face
BeamLoad right-click optoins
BeamLoad changing load type

## Slide 36
Components
3 Loads: FaceLoad component
”FaceLoad” component:
Right-click menu to toggle between load types: Uniform, Variable, Point or Edge
Static inputs for load case, element list, axis, direction and projection (with defaults)
Input adapts to the selected load type:
3 Loads
Gravity
Node
Beam
Face
FaceLoad right-click optoins
FaceLoad changing load type

## Slide 37
Components
4 Analysis: Analyse component
”Analyse” component:
Will/should be able to merge model inputs, so that users can append to existing models
Takes all the inputs from categories 1, 2 and 3 and assembles a model
Different analysis methods (and their settings) still to be developed/implimented
Potential to have option to ”send to GsaCloud” for analysis
Task & combinations (still to be developed)
Analysis component
4 Analyse
Analyse
Tasks
Combinations

## Slide 38
Components
6 File: Save component
”Save” component:
Save if no input to file
Save as if file has input
Double-click component to automatically open the file in GSA
Spekle (still to be developed) – plug GSA output directly to speckle
Save component – double-click to open file in GSA!
6 Output
Save
Speckle

## Slide 39
GsaGH current component overview

## Slide 40
GsaGH Components test-run

## Slide 41
Next steps
GsaGH ideas braindump
Short term
Analysis
  Implement setting up analysis tasks
  Implement ability to run analysis
Results
  Extract numbers
Continue Alpha-testing / bug fixes / implement new GsaAPI updates
Review everything (code, architecture, UI)
Get funding!
Long term
Analysis
  Support GsaCloud
  Find a way to run analysis locally on multiple cores without affecting Rhino/Grasshopper performance while running
  Load combinations (need a proper UI pop-up is my guess)
Develop/design better component UI
Speckle support (open/save)